Instructions and Maintenance Manual

FOR HYDRAULIC SCISSOR LIFT

TDY-P3010

The specifications stated on this brochure are not binding. We reserve the right to change the specification without notice

Disclaimer

No part of this book shall be reproduced, stored in retrieval, or transmitted by any means, electronic, mechanical, photocopying, recording, or otherwise without the written permission of TONGDA auto maintenance equipment Co,.LTD. While every precaution has been taken in the preparation of this manual, the publisher assumes no responsibility for errors or omissions. Neither is any liability assumed for damages resulting from the use of information contained herein.

This document is the proprietary information of TONGDA auto maintenance equipment Co,.LTD. furnished for customer use only. No other uses are authorised without written permission from TONGDA auto maintenance equipment Co,.LTD.

TONGDA auto maintenance equipment Co,.LTD. reserves the right to make changes, without notice to this document and the products are describe. TONGDA auto maintenance equipment Co,.LTD. or it’s distributors shall not be liable for technical or editorial errors or omissions made herein; nor for incidental or consequential damages resulting from the furnishing performances, or use of this document.

This manual contains information that is correct to the best knowledge of TONGDA auto maintenance equipment Co,.LTD. It is intended to be a guide and should not be considered as a sole source of technical instruction. It should not replace good technical judgment since all possible situations cannot be anticipated. If there is any doubt as to the exact installation, configuration, and/or use, please call TONGDA auto maintenance equipment Co,.LTD. or its distributor.

The choice of system component is the responsibility of the buyer, and how they are used cannot be the liability of TONGDA auto maintenance equipment Co,.LTD. or its distributors. Assembly, installation, commissioning, initial adjustment and testing, or any work relating to EXTRAORDINARY maintenance, repair, overhauls, transport and dismantling of the Lift must be performed by specialist personnel from the authorised to commission, install and dismantle Lifts.

The manufacturer and its distributors decline all responsibility for injury to persons or damage to vehicles or objects when any of the above mentioned operations have been performed by unauthorised personnel or when the rack has been subject to abuse.

This manual explains the operational and safety aspects that may prove useful to the Operator and Maintenance personnel. It will give a better understanding of the structure and operation of the Lift and the best use of the Lift. The operator should familiarise himself with the technical and safety aspects of the Lift to be competent in operating the Lift.

The words “Operator” and “Maintenance Fitter” used in this manual are construed as follows:

OPERATOR: person authorised to use the Lift. The Lift must be operated in the correct manner as indicated

MAINTENANCE FITTER: person authorized for routine maintenance of the Lift.

The end user can only use the Lift in the correct manner to which it is intended as defined in the instructions.

Loose clothing should not be worn when operating the Lift. Any personnel with long hair operating the Lift should use a protection cap as precautionary safety measures.

******* IMPORTANT NOTE ********

The following must be observed at all times to ensure correct use of the hoist.

- Follow regular maintenance schedule as per manual

- Ensure safety precautions are taken and use the hoist in accordance with the manufactures instructions

- It is the Owner’s responsibility to ensure all safety regulations and work cover requirements are met to satisfy all state laws

IMPORTANT MANUAL INFORMATION

Particularly important information is distinguished in this manual by the following notations:

NOTE:

- This manual should be considered a permanent part of this lift and should remain with it even if the lift is subsequently sold.

- We continually seeks advancements in product design and quality. Therefore, while this manual contains the most current product information available at the time of printing, there may be minor discrepancies between your lift and this manual. If you have any questions concerning this manual, please consult your dealer or call manufacturing.

TABLE OF CONTENTS

1、	SAFETY INFORMATION	５

2、	TRANSPORT & UNPACKING	６

3、	SPECIFICATIONS	７

4、	WORKING PLACE	８

5、	DESCRIPTION	８

6、	INSTALLATION	９

7、	OPERATION	１０

8、	STORING	１１

9、	MAINTENANCE	１２

10、	HYDAULIC POWER UNIT	１３

11、	ELECTRIC  SYSTEM	１５

12、	HYDRAULIC  SYSTEM	１４

13、	STRUCTURE DIAGRAM	１７

# SAFETY INFORMATION

THIS SCISSOR LIFT IS A KIND OF LIFTING EQUIPMENTS. TO MAKE SURE ITS SAFE WHEN OPERATE DEPEND ON THE TECHNIQUES AS WELL AS   THE EXPERTISE OF THE OPERATOR. EVERY OPERATOR SHOULD KNOW  THE FOLLOWING REQUIREMENTS BEFORE OPERATE THE LIFT.

THEY SHOULD:

□    OBTAIN THOROUGH INSTRUCTIONS FROM A COMPETENT SOURCE ON ALL ASPECTS OF LIFT OPERATION.

□    OBSERVE THE WARNINGS AND MAINTENANCE REQUIREMENTS IN THE OWNER'S MANUAL.

□    OBTAIN QUALIFIED TRAINING IN SAFE AND PROPER OPERATION TECHNIQUES.

□    OBTAIN PROFESSIONAL TECHNICAL SERVICE AS INDICATED BY THE OWNER'S MANUAL AND/OR WHEN MADE NECESSARY BY MECHANICAL CONDITIONS.

Please read the following important notice carefully before operate the lift.

Lifting Capacity: 3000KG

WARNING: When the lift is working, any personnel is not allowed to get in the lift and the car, it could result in severe injury or death!

DO NOT PUT ANYTHING ON THE SAFETY LOCK.

# TRANSPORT & UNPACKING

Depending on the standard request, this lift and the hydraulic pump are protected by two cartons with pallets. And the machine must be handled with a forklift with the forks positioned as shown fill the figure.

●  Shipping weight for the lift is 520KG.

●  Shipping weight for the hydraulic pump is 80KG.

Once the packing material has been removed, check the machine for any things of damage.

Keep the packing materials out of the reach of children as they can be a source of danger.

● Keep the packing for possible future transport.

# SPECIFICATIONS

| Lifting capacity | 3000kg/3500KG |
| --- | --- |
| Max. Lifting height | 1000mm |
| Min. height | 110mm |
| Overall width | 1760mm |
| Platform length | 1400-1900mm |
| Space between platforms | 700mm |
| Lifting time | 60 sec |
| Noise | 70db (A) 1m |
| Operating temperature | 10°C - +50°C |
| Work environment: | Closed room |
| Power supply | 2.2KW (240v, 415v) |
| Gross weight | 600kg |
| Net weight | 550kg |

DIMENSIONS AND OVERALL CLEARANCE DIAGRAM

# WORKING PLACE

Choose the place that the machine can be installed in compliance with current work place safety regulations. The floor should not be broken or uneven so that the machine will be stable and the platform can move freely.

If the install at out, it must be protected by some kind of roofing against rain.

The following work environment conditions are applicable

- Relative humidity: from 30-95% without condensation.

- Temperature: 10-50℃.

The machine can not be operated in explosive atmospheres.

WORKPLACE  REQUIREMENTS

Machine need space: requirements are 3200X2000mm with a minimum distance from walls as shown in the diagram.

These measurements are also the machine working range. Persons other than specially trained and authorized operators are expressly forbidden to enter this area.

# DESCRIPTION

PUMP

NOTE

It is the main parts figures above. More detailed components and assembly please see exploded view.

# INSTALLATION

Connecting pipes

There are two pipes from the hydraulic pump as shown in the figure. (X) is a electric pipe and used for the safety lock. (Y) is a hydraulic oil pipe and used for the hydraulic cylinders.

Enter hydraulic oil

Remove the motor box off, and then turn the oil cap anti-clockwise to open the oil inlet. Fill in the hydraulic oil 30# from the oil inlet as shown in the figure.

NOTE

- Make sure that there is sufficient oil in the tank when the machine in working

- Do not overfill the oil tank, otherwise it may overflow when the oil warms up and expands.

- Make sure that the oil tank cap is properly closed before working.

# OPERATION

During all operations, keep hands and other parts of the body as far as possible from moving parts of the machine. With necklace, bracelets and too large clothes, can be dangerous for the operator.

Press the UP button,

the lift will go up

When the lift is working (lifting a car), remember:

any personnel do not get in the lift and the car, it could result in severe injury or death!

Press the DOWN button,

the platform will go down

.

# STORING

If the machine has to be stored for a long time you should :

- Get down the platforms and no heavy object on them.

- Disconnect the machine from all power sources.

- Grease all the parts that could be damaged if they dry out.

- Empty hydraulic oil tank and wrap the machine in a sheet of protective plastic to prevent dust from reaching the internal working parts.

If the machine has to work again after a long storing period, it is necessary to:

- put the oil into the tank again.

- restore the electric connection.

# MAINTENANCE

###### PRECAUTIONS

WARNING

Maintenance must be carried out only by skilled personnel who are very familiar with the lift.

When performing maintenance on the lift, follow all the necessary precautions to prevent the lift from being started accidentally:

1. Cut off the power and pull the plug out of the jack.

2. While maintenance is being performed on the machine, always keep in mind all the main possible risks and the safety instructions indicated in chapter 3 “safety risk of electric shock” at the machine power supply terminal strip.

IT IS PROHIBITED TO PERRORM MAINTENANCE ON THE OIL CYLINDER. IT SHOULD BE REPLACED WHEN DAMAGED.

IMPORTANT

1. Only use original spare parts and tools that are suitable for the job and in good condition;

2.Follow the maintenance schedule indicated in the manual: these frequencies are indicative and must always be considered as general rules to be respected.

3.Good preventive maintenance requires constant attention and continuous supervision on the machine. Quickly find the cause of any abnormalities such as excessive noise, overheating, leaking fluids, etc.

Special attention is required for:

- The condition of lifting parts (cylinder, power unit);

- Safety devices (oil cylinder and safety wedges)

To perform maintenance correctly, refer to the following documents supplied by the lift manufacturer:

1. Complete functional diagram of the electric equipment and auxiliary equipment indicating the power supply connections

2. Hydraulic diagram with lists of parts and max. Pressure values

3. Exploded drawings with the data needed to order spare parts

PERIODIC MAINTENANCE

OPERATION FREQUENCY

To keep the lift working at full efficiency, follow the indicated maintenance schedule. The manufacturer will not be responsible and will not honor the warranty as a result of

non-compliance with the instructions indicated above.

NOTE

The frequency indicated refers to normal operating conditions; different frequencies will apply to particularly server conditions.

ALL MAINTENANCE OPERATIONS MUST BE PERFORMED WITH THE LIFT STOPPING OR THE MAIN SWITCH PLACED AT “O”.

When after the machine has been installed, check:

- That the opposite carriages arms are at the same level

- The power unit oil level. Add oil up to the right level, if necessary

- EVERY MONTH

# HYDAULIC POWER UNIT

- Check the oil level in the tank, using the special dipstick, which is attached to the filler cap. If necessary, add oil through the cap to reach the required level. For the type of oil, see “TECHNICAL SPECIFICATIONS”.

- After the first 40 hours of operation, check the press oil contamination level. (Clean the filter and replace the oil if there is a high contamination level).

###### HYDRAULIC CIRCUIT

Check that there are no oil leaks in the circuit between the power unit and cylinder and in the cylinder itself. In this case, check the condition of the gaskets and replace them, if necessary.

###### HYDRAULIC PUMP

Under normal operating conditions, check that there is no change in the noise in the motor and gear pump and check that the relative bolts are properly tightened.

SAFETY SYSTEMS

- Check the operating condition and efficiency of the safety devices .

- Use a torque wrench to check that the post bases anchor bolts screws are properly tightened to the ground as well as the connection bolts.

- Clean and lubricate the carriage side runners and guides.

- Check that all screws are tightened

- Check that the locking system works properly.

- Grease all the moving parts.

EVERY 6-MONTHS…

###### HYDRAULIC

Check the contamination or aging level of the oil. Contaminated oil is the main cause of malfunctions of the valves and leads to a brief service life of the gear pumps.

EVERY 12- MONTHS

General check: visual inspection of all structural parts and mechanisms to guarantee that there are no problems or abnormalities.

Electric plant: skilled electricians (contact the service center) should test the electric plant, including the motor of the power unit, and control box.

###### HYDRULIC PLANT OIL

Replace the oil, following the instructions listed below:

- Lower the lift to the minimum height (on the ground)

- Make sure that the hydraulic cylinder is at the end of its travel

- Disconnect the power supply to the lift rack.

- Drain the oil from the hydraulic circuit, unscrewing the plug located at the bottom of the power unit reservoir.

- Close the drain plug

- Fill the hydraulic station oil cylinder with oil throng the plug located at the top of the hydraulic station.

The oil must be filtered.

Oil characteristics and types are reported in the technical specifications.

- Close the filler plug

- Energize the lift

- Go through two or three up-down cycles (for a height about 20-30 centimeters) to insert oil into the circuit.

When changing the oil: use only recommend oil or the equivalent; do not use deteriorated oil that has been in the warehouse for an extended period of time.

AFTER EACH MAINTENANCE OPERATION, THE MACHINE MUST RETURN TO ITS INITIAL CONDITIONS, INCLUDING THE DISASSEMBLEED PROTECTION AND SAFETY DEVICE.

To ensure good maintenance, it is important:

- To sue only tools that are suitable for the job and original spare parts

- Follow the minimum maintenance schedule as indicated

- Immediately find the cause of any abnormalities (excessive noise, overheating, leaking fluids, etc)

- Pay special attention to lifting parts (cylinders) and safety devices

- Use all the documentation supplied by the manufacturer (wiring diagrams, etc)

# HYDRAULIC  SYSTEM

- Oil cylinder 1

- Oil cylinder 2

- Descending valve

- Slipping valve

- Throttle valve

- Retaining valve

- Motor

- Pump station

- Oil filter

- Oil Tank

- safe valve

# ELECTRIC  SYSTEM

YA

| QS | Power switch | SB2 | Downside button |
| --- | --- | --- | --- |
| QF | Circuit interrupter | SB3 | Tooth lock button |
| QF1 | Circuit interrupter | KM | A.C. contactor |
| TC | Transformer | KA | intermediate relay |
| VC | rectifier bridge | KT | Time relay |
| HL | Indicator | QV | Three-way magnetic valve (Pneumatic) |
| SB1 | Upside button | YV | electromagnetic unloading valve (Hydraulic) |

Refer to the above circuit diagram for the connection of the motor.
The rotation of the motor should be towards the direction of the pump, if not, amend the connection of motor.

# STRUCTURE DIAGRAM

| Code | Name | Code | Name |
| --- | --- | --- | --- |
| 101 | Platform assembly | B6 | Cylinder |
| 102 | Front plate | B7 | M5×25 inner hexagonal bolt |
| 103 | Front plate trolley | B8 | 3030 oilless bearing |
| 104 | Support for front plate | B9 | 2530 oilless bearing |
| 105 | Fasten axle for front plate | B10 | cylinder |
| A1 | Φ12 circlip | 301 | Outside scissor frame |
| 201 | Inside scissor frame assembly | 302 | Trolley for outside scissor |
| 202 | Middle axle of scissor | 303 | Trolley axle for outside scissor |
| 203 | Fasten plate for trolley axle of inside scissor | C1 | 2515oilless bearing |
| 204 | Lock hook | C2 | Φ25 circlip |
| 205 | Trolley axle for inside scissor | 401 | Bed plate assembly |
| 206 | Trolley for outside scissor | 402 | Fasten base on the outside of Outside scissor |
| 207 | Fasten axle for inside scissor | 403 | Fasten base on the inside of Outside scissor |
| 208 | Assistant arm | 404 | Trolley base plate for inside scissor |
| 209 | Top-shaft for cylinder | D1 | M10×55 inner hexagonal bolt |
| 210 | bottom-shaft for cylinder | D2 | Φ10 grease cup |
| B1 | Φ30 circlip | D3 | M8×12 sunk screw |
| B2 | M6×12 inner hexagonal bolt | 501 | pipeline for long cylinder |
| B3 | 3050 oilless bearing | 502 | Pipeline for short cylinder |
| B4 | M6×12 inner hexagonal locking bolt | 503 | pipeline for Pump station |
| B5 | 2515 oilless bearing |  |  |

# Text boxes

CAUTION

Press the UP button,

the lift will go up

Press the UP button,

the lift will go up

YA

YA